## Slide 1: PPE & N95 Management: Key Questions/Considerations
HCI Infection Control Team
Scope: PPE and Respiratory Protection while caring for COVID19 Patients.
Key Issues
  Who actually needs Respiratory Protection (RP)?
  What are the Normal v. Contingency RP Considerations?
  How should we maintain PPE discipline?
  CDC Strategies for Optimizing the supply of RP.
  What are the Alternatives for a N95?

## Slide 2: Infection Control Team Members
Marla Clifton
Kathleen DeRoos
Craig Brown
Wendy Kady
Robert Pearlman
Gio Baracco
Carter Mecher
Troy Knighton
Ben Guerrero

## Slide 3: COVID-19: How can we protect Veterans and staff?
Personal Protective Equipment
For the most current CDC recommendations on Personal Protective Equipment, visit: https://www.cdc.gov/coronavirus/2019-ncov/infection-control/control-recommendations.html
For CDC guidance on donning (putting on) and doffing (taking off) PPE safely: https://www.cdc.gov/hai/prevent/ppe.html
Note: PPE recommendations may differ by setting and type of exposure, and may change as knowledge of the virus evolves.

## Slide 4: COVID19: Who Needs a Respirator (N95 or higher)?
Clinicians who are directly caring for an infectious patient
  Spread of respiratory viruses from person-to-person happens among close contacts (within 6 feet)
  Aerosol generating medical procedures (AGMP) with an infectious patient
    RP
    Eye protection
    Gowns
    Gloves
In other care areas the significant risk will be environmental transmission from fomites
  Use excellent hand hygiene or alcohol hand rub
  Don’t touch your face
  Routine environmental surface cleaning/disinfection

## Slide 5: Normal v. Contingency RPP Considerations
Limit who is enrolled in RPP by risk potential for occupational exposure.
The more people enrolled the
  More medical clearances required
  More fit testing are required
    More time it will take to complete
    More RP you burn through
    Less RP you will have for care of infectious patients
The more changes to different respirator models & sizes the more fit testing required for all classes of respirator.
Notes: Strategies for optimizing PPE: https://www.cdc.gov/coronavirus/2019-ncov/hcp/respirator-supply-strategies.html

## Slide 6: New OSHA Guidance on COVID19 and Fit Testing Posted March14, 2020
OSHA suggested that annual fit testing may be suspended if:
  Make a good faith effort in complying with 19CFR1910.134
  Use only NIOSH certified RP
  Implement CDC and OSHA Strategies for Optimizing Supply of N95s
  If a previous fit tests exists with the same model, style, and size of RP that is used to respond to COVID19
  Inform workers that employer is suspending annual fit testing
  Explain to workers the importance of the user seal check
  Conduct a fit test if employee changes in physical condition that could affect RP seal
  Remind workers that they should inform supervisor if the integrity and or fit of filtering facepiece is compromised.
  https://www.osha.gov/memos/2020-03-14/temporary-enforcement-guidance-healthcare-respiratory-protection-annual-fit

## Slide 7: Maintain PPE Discipline
Assign a team who is capable to manage supplies, who will:
  Establish a burn rate of PPE
  Tracks who requests and how much by work area
  Protect PPE from theft (MAJOR ISSUE)
  Lock up PPE and monitor who has access – Guard 24/7
  Ensures service lines requesting PPE have a legitimate need
    Resist providing to those that don’t provide care of infectious patients
Considerations for reducing burn rate:
  Limit the number of staff who provides direct care of infectious patients
  ASK, Is it absolutely necessary for that number of staff to enter the AIIR or Cohort care area ?
    Could other services, i.e. Social Work be done by video chat?
  Cohort multiple patients in a large room to reduce donning and doffing PPE
  NOTE: Exiting/entering individual AIIR requires the clinician to don/doff PPE between rooms

## Slide 8: CDC STRATEGIES FOR OPTIMIZING SUPPLY OF N95 RESPIRATORS
Conventional Capacity
Contingency Capacity
Crisis Alternate Strategies
Notes: https://www.cdc.gov/coronavirus/2019-ncov/hcp/respirators-strategy/index.html

## Slide 9: RPP Strategy Decisions
Consider
  Status of PPE & N95/respirator inventory
  Status of your supply chain
  What are the PPE & N95/respirator burn rates
Keep in mind - Reality
  What the potential situation will look like in a month from now
  Assume no resupply within the month
  You may NOT have experienced the patient surge, yet
Most of our facilities are experiencing PRE surge
The Strategies may be applicable for supply of other PPE

## Slide 10: CONVENTIONAL CAPACITY Strategy
Criteria
  Normal continuum of care practices w/o limited resources
Hierarchy of Controls
  Engineering Controls
    AII Rooms
    Physical Barriers
  Administrative Controls
    Patient / visitor access and source control (masking)
    Exclude all HCP not directly involved in patient care
  Personal Protective Equipment
    N95
    Surgical N95s only for direct patient care setting with airborne fluid hazards (e.g., splashes, sprays)
    Use alternatives where feasible
NOTE: Surgical 95 is irrelevant in treating COVID19, only relevant in where pressurized spray or stream of blood environment, ie. Surgery or ED
Do these first!
Notes: https://www.cdc.gov/coronavirus/2019-ncov/hcp/respirators-strategy/conventional-capacity-strategies.html

## Slide 11: Aerosol-Generating Medical Procedures (AGMPs)
Any procedure carried out on a patient that can induce the production of aerosols of various sizes, including droplet nuclei.
Examples of AGMPs include, but are not limited to:
  Collection of Nasopharyngeal cultures/swabs, per CDC
  Non-invasive positive pressure ventilation (BIPAP)
  Continuous positive airway pressure (CPAP)
  Endotracheal intubation; respiratory/airway suctioning
  High-frequency oscillatory ventilation
  Tracheostomy care
  Chest physiotherapy
  Aerosolized or nebulized medication administration
  Diagnostic sputum induction; bronchoscopy procedure
  Autopsy of lung tissue

## Slide 12: CONTINGENCY CAPACITY Strategy
Criteria
  No significant impact on care or safety of the HCP
  Potential impending shortage of N95 respirators
Administrative Controls
  Decrease length of stay for medically stable patients
Personal Protective Equipment
  Extended Use (cohorted groups)
    Wearing the same N95 respirator and/or other PPE for repeated close contact encounters, without doffing the respirator/PPE between encounters
  Use Beyond Manufactures Shelf Life for fit-testing/training – During Contingency Capacity Strategy
Notes: https://www.cdc.gov/coronavirus/2019-ncov/hcp/respirators-strategy/contingency-capacity-strategies.html

## Slide 13: CRISIS ALTERNATE Strategy
Criteria
  Not commensurate with U.S. standards of care
  Periods of expected or known shortages
Personal Protective Equipment
  Use Beyond Manufactures Self Life RP for HCP – During Crisis Alternate Strategy
  Cohorted patients
  Limited re-use of respirators for direct patient care
    Same respirator used by one HCP for multiple encounters with different patients but doffing after each encounter
  Use foreign certified RP
Prioritizing use by activity type (distance & care)
When respirators are no longer available
  See CDC Guidelines
Notes: https://www.cdc.gov/coronavirus/2019-ncov/hcp/respirators-strategy/crisis-alternate-strategies.html

## Slide 14: Crisis Alternate Strategy Facemask v. Respirator
Notes: https://www.cdc.gov/coronavirus/2019-ncov/hcp/respirators-strategy/crisis-alternate-strategies.html

## Slide 15: BEYOND MANUFACTURER DESIGNATED SELF LIFE
CDC’S Release of Stockpiled N95 Filtering Facepiece Respirators Beyond the Manufacturer-Designated Shelf Life: Considerations for the COVID-19 Response
FDA Coronavirus Disease 2019 (COVID-19) Emergency Use Authorization Information
  Appendix B List of Authorized Surgical N95s

## Slide 16: What Are the Alternatives to N95s
Particulate filter designations
Filter designations that may be used in Healthcare
Potential Courses of Action between different types of air purifying respirators

## Slide 17: RP Particulate Filters
Formerly
HEPA
Efficiency – Filters out the most penetrating aerosol size (approximately 0.3 micrometer)
Notes: https://www.cdc.gov/coronavirus/2019-ncov/hcp/respirator-use-faq.html
The first part of the filter's classification uses the letters N, R, or P to indicate the filter's ability to function when exposed to oils. "N" means Not resistant to oil; "R" means somewhat Resistant to oil; and "P" means strongly resistant to oil, or oil-Proof.
This rating is only important in work settings where oils may be present, because some oils can reduce the effectiveness of the filter.
The second part of the classification -- the number-- refers to the filter's ability to remove the most-penetrating particle size during "worst case" testing.
Filters that remove at least 95 percent of these particles are given a 95 rating. Those that filter out at least 99 percent receive a 99 rating, and those that filter out at least 99.97 percent - essentially 100 percent - receive a 100 rating.
Using this classification method, an N95 filter is not resistant to oil and removes at least 95 percent of the most-penetrating particles.

## Slide 18: Which filter designation can be used in healthcare environment?
An N-95 is preferred by healthcare for its effectiveness and low cost, except for surgery and other invasive procedures areas.
  N-95s have the lowest efficiency rating.
  Oil rating in healthcare is NOT a concern.
All other respirator efficiencies and oil proof designations are effective.
CDC recommends all other NIOSH certified efficiencies and oil ratings in their guidance for Covid-19.
Notes: https://www.cdc.gov/niosh/npptl/topics/respirators/factsheets/respsars.html

## Slide 19: Course of Action 1: Order Different Models of Filtering Facepieces
Positives
  All efficiencies are relevant
  Oil rating is NOT relevant
  Higher efficiencies are more protective
  Disposable
  Same training as N-95
Negatives
  Higher the efficiency the higher the cost
  Higher the efficiency the higher the resistance to breathing
  Higher the oil rating the higher the cost
  Air could be more moist or hotter while breathing inside the mask
Higher the efficiency and oil rating the more it’s likely going available for purchase.

## Slide 20: Course of Action 2: Order PAPRs
Positives
  If loose fitting hood – No fit testing required
  Excellent protection
  Reusable
  Excellent to use as a buffer for fit testing
Negatives
  Should not use if sterile field is required or if HCW may be infectious to patient
  Most expensive option >$800 per unit
  Requires more respirator and battery maintenance
  If batteries stored for long time the potential for of a weak charge and capacity of battery life may be reduced.
  Depending on model decontamination could be complex; therefore, higher potential for HCW getting infected
  Bulky
  Could intimidate the patient
  If PAPR is used in one area and other areas a N-95, there could give the perception that one group is getting better protected than others, respectively

## Slide 21: Course of Action 3: Order Elastomeric Respirators
Positives
  Better fitting than filtering facepieces
  Better protection than N-95
  Respirator is cleanable & reusable
  In some cases the filter housing can be decontaminated; therefore, reuse filter might be an option
  Configurable N, P, R & 95, 99, 100
  Easier to exhale than N-95
Negatives
  Should not use if sterile field is required or if HCW may be infectious to patient
  Requires some low intensive maintenance
  More expensive than N-95 but less than PAPR
  Requires more training than N-95
  Depending on the make and model it can be complex to clean – no standardized cleaning protocol from CDC
  Harder to communicate with elastomeric respirators
  Could intimidate the patient

## Slide 22: In the end it’s the seal that matters. All other filter efficiencies are an option.

## Slide 23: PPE & N95 Management
HCI Infection Control Team
Scope: PPE and Respiratory Protection while caring for COVID19 Patients.
Key Issues
  Who actually needs an Respiratory Protection (RP)?
  What are the Normal v. Contingency RP Considerations?
  How should we maintain PPE discipline?
  CDC Strategies for Optimizing the supply of RP?
  What are the Alternatives for a N95